|  | EVALUATION CHECKLIST FOR THE ACCREDITATION OF PRACTICAL ASSESSMENT CENTER ANNEX 4 – EVALUATION INSTRUMENTS FOR ENGINE SIMULATOR |
| --- | --- |

| Name of Company or Corporation: | Contact Number: | Company Address: |
| --- | --- | --- |
| Date & Time Commenced of Inspection: | Date & Time Completed Inspection: |  |
| Company E-mail : | MARINA Control Number: |  |

| Item No. | Simulator Performance Standards | Applicant Self Evaluation ( √ ) | Evaluator Verification ( √ ) | Remarks |
| --- | --- | --- | --- | --- |
| BEHAVIORAL REALISM (ENGINE) |
|  | The simulator models shall be able to replicate the dynamic behaviour of the machinery systems and all its visual parameters as well as the interactions between the sub-systems. |  |  |  |
|  | The simulator models shall simulate the engine room components with their procedures, as well as modelled controller systems (sensors, controllers, actuators, and valves) connected to the processes. |  |  |  |
|  | When simulating real equipment the behaviour of such simulated equipment should behave as identical aw possible as the original. Critical parameters of the behaviour shall be documented |  |  |  |
|  | The simulator model shall make applicable controllers available and adjustable with regards to PID (proportional-integral-derivative controller) parameters. |  |  |  |
|  | The simulator model shall provide facilities to allow the injection and resetting of malfunctions at appropriate times during operation as necessary. |  |  |  |
|  | It shall be possible to simulate change in seawater temperature and demonstrate how this affects the complete simulation model. |  |  |  |
|  | It shall be possible to simulate a change in air temperature and demonstrate how this affects the complete simulation model. |  |  |  |
|  | The simulator shall have all heat exchangers available and adjustable with regards to their parameters (heat-transfer factor, heat dissipation are etc.) |  |  |  |
|  | The simulator shall make all pumps available and adjustable with regards to their parameters (pump capacity, wear, etc.) |  |  |  |
|  | It shall be possible to demonstrate systematically the tests that are made on the UMS (Unmanned Machinery Space) alarm system. |  |  |  |
|  | It shall be possible to simulate auto slow-down and emergency shut down |  |  |  |
|  | It shall be possible to simulate safe methods to test Inert Gas Generator (IG) alarms and control. |  |  |  |
|  | It shall be possible to simulate testing of the 24V D.C. power supply to the navigation, communication and engine room control console in event of power failure. |  |  |  |
|  | It shall be possible to simulate safe method of testing the insulation for rotor and stator. |  |  |  |
|  | It shall be possible to simulate of reading a power factor meter with reference to four segments |  |  |  |
|  | It shall be possible to simulate testing of the devices and relays provided for generator protection |  |  |  |
|  | It shall be possible to simulate tests related to AVR (Automatic Voltage Regulator) |  |  |  |
|  | It shall be possible to simulate methods of cooling and checking of air gap |  |  |  |
|  | It shall be possible to simulate the precautionary measures when megger testing the rotor of a brushless generator |  |  |  |
|  | It shall be possible to simulate routine tests on an emergency generator |  |  |  |
|  | It shall be possible to simulate how a generator circuit breaker OCR (Over Current Relay) is set and tested. |  |  |  |
|  | It shall be possible to simulate the process of connecting a shaft generator on load and specific conditions for taking off load. |  |  |  |
|  | It shall be possible to simulate the procedure for megger testing a high voltage system |  |  |  |
|  | It shall be possible to simulate the maintenance and checks carried out on an ACB (Air Circuit Breaker) |  |  |  |
|  | It shall be possible to simulate recovery from “dead ship” condition. |  |  |  |
|  | It shall be possible to simulate methods test the “Preferential Tripping Sequence” |  |  |  |
|  | It shall be possible to simulate methods to tests auto “Cut In” of stand fault |  |  |  |
|  | It shall be possible to simulate methods of diagnosing single phasing fault. |  |  |  |
|  | It shall be possible to simulate operation and maintenance of variable speed motor starters. |  |  |  |
|  | It shall be possible to simulate operational test methods of oily water separator monitors |  |  |  |
|  | It shall be possible to simulate test methods for level alarms and function tests of bilge pumping arrangement |  |  |  |
|  | It shall be possible to simulate the functional tests of ODMCS (Oil discharge monitoring and control system) and ODME (Oil discharge monitoring equipment) system |  |  |  |
|  | It shall be possible to simulate the function test of OWS (Oily water separator) and PPM (Parts per million) unit. |  |  |  |
| PHYSICAL REALISM |
| LOW SPEED ENGINE |
|  | The simulated engine room shall as a minimum reflect typical machinery found on merchant ships. The following main components shall be simulated and all necessary sub-systems included for a low speed engine: Main engine including turbocharger system |  |  |  |
|  | 2 auxiliary diesel generators |  |  |  |
|  | Lubrication oil separator |  |  |  |
|  | Steering gear system |  |  |  |
|  | Fire pump |  |  |  |
|  | Shaft generator |  |  |  |
|  | Cooling water system including freshwater generation system |  |  |  |
|  | Turbo generator |  |  |  |
|  | Fuel oil bunkering system |  |  |  |
|  | Fuel oil settling and service systems |  |  |  |
|  | 2 heavy fuel oil separators |  |  |  |
|  | 1 diesel oil separator |  |  |  |
|  | Steam generation plant including exhaust and oil-fired boilers |  |  |  |
|  | Diesel oil and heavy fuel oil supply to main and auxiliary engines |  |  |  |
|  | Main engine operation from engine room, engine control room and bridge |  |  |  |
|  | Turbocharger system |  |  |  |
|  | Air ventilation system for engine and control room |  |  |  |
|  | Bilge water system including oily water treatment systems |  |  |  |
|  | Stern tube system |  |  |  |
|  | Deck machinery applicable to the ship model |  |  |  |
|  | Ballast system |  |  |  |
|  | Sewage treatment system |  |  |  |
| MEDIUM AND HIGH SPEED ENGINE |
|  | The simulated engine room shall consist of typical machinery found on merchant ships. The following main components shall be simulated and all necessary sub-systems included for a medium and high speed engine: One or more main engines |  |  |  |
|  | Main SW system |  |  |  |
|  | 2 auxiliary engines |  |  |  |
|  | Fuel oil tanks |  |  |  |
|  | Fuel oil separator |  |  |  |
|  | Lubrication oil separator |  |  |  |
|  | Main engine(s), including: Fresh water system Lubrication system Turbocharger system ME SW system |  |  |  |
|  | Reduction gear system |  |  |  |
|  | Controllable propeller pitch were applicable |  |  |  |
|  | Steam generation system as applicable |  |  |  |
|  | Freshwater generator |  |  |  |
|  | Bilge wells and bilge separation system |  |  |  |
|  | 2 air compressors |  |  |  |
|  | Steering gear system |  |  |  |
|  | Fire pump |  |  |  |
|  | Electrical power plant |  |  |  |
|  | Deck machinery applicable to the ship model |  |  |  |
|  | Ballast system |  |  |  |
|  | Sewage treatment system |  |  |  |
| MACHINERY SPACES |
|  | The simulated machinery spaces shall at least include one dedicated room for this purpose. |  |  |  |
|  | At least the following main components of the machinery spaces shall be graphically presented or represented by mock-ups or in realistic visualization (to illustrate physical presence) in the simulated machinery spaces: Main engine |  |  |  |
|  | Auxiliary diesel generators |  |  |  |
|  | Steam boiler |  |  |  |
|  | Fire pump |  |  |  |
|  | The facilities for local operation in the simulated machinery spaces shall consist of local operating stations for each system. Each station shall be furnished with start/stop (open/closed) buttons and status lights, various numbers of pressure -, temperature indicators, etc. The local operating stations shall at least give means to operate the following: Main engine (ME) |  |  |  |
|  | ME lubricating oil systems including separator |  |  |  |
|  | ME fresh water cooling system |  |  |  |
|  | ME sea water cooling system |  |  |  |
|  | ME auxiliary blowers |  |  |  |
|  | 2 auxiliary diesel generators |  |  |  |
|  | Steam boiler |  |  |  |
|  | Fuel oil system (diesel and heavy fuel oil) including separator |  |  |  |
|  | 2 air compressors |  |  |  |
|  | Steering gear system |  |  |  |
|  | Bilge water system |  |  |  |
|  | Fire pump |  |  |  |
|  | All valves typically associated with the operation of above machinery may be operated at the computer screen in a 3D visual form or mouse operated by the candidate. |  |  |  |
|  | Internal communication system. |  |  |  |
| OPERATING ENVIRONMENT |
|  | It shall be to adjust the noise level in the simulated machinery spaces infinite from no added noise up to minimum 100 Db(A). The noise shall have a frequency distribution typical for machinery spaces. Headset is provided for each work station. |  |  |  |
|  | It shall be possible to simulate the sea water temperature at least infinite between +1ºC and +30 ºC |  |  |  |
|  | An alarm can be heard through headset of a candidate and by flashing light in the machinery spaces |  |  |  |

X- FINDINGS: Please use Annex 5

EVALUATED BY:

| Signature Over Printed Name Team Leader |  | Signature Over Printed Name BOMDO / BOMEO |  | Signature Over Printed Name BOMDO / BOMEO |
| --- | --- | --- | --- | --- |
| Team Members: |  |  |  |  |
| (Signature Over Printed Name) |  | (Signature Over Printed Name) |  | (Signature Over Printed Name) |

CONFORME: __________________________________________ Signature Over Printed Name Company Representative

# Text boxes

MARITIME INDUSTRY AUTHORITY

REPUBLIC OF THE PHILIPPINES

DEPARTMENT OF TRANSPORTATION

BOE NO.: 04-00

Initial Issue Date: 09-08-2017

Revision Date: 00